        E F C L C H A N N E L I Z E R
        v0.1 2016

WHAT IT IS

  This is a library and a stand-alone program that can split input signal
  stream into a number of equally spaced channels. The samples are complex
  valued single precision floats. If Fs is a sampling frequency, the
  channels' center frequencies will be 0, Fs/C, 2*Fs/C, ... (C-1)*Fs/C,
  where C is the number of channels. The output can be optionally decimated
  by an integer factor D (typically D=C).

  The library is designed for high throughput, using on-the-fly compiled
  assembly codelets that get compiled are tuned for a particular machine and
  C and D parameters when the program starts. The compiled codelet is then
  dynamically linked with the main program so that the channelizer could use
  it. The assembly heavily relies on using SIMD instructions, the flavor of
  which (SSE, AVX or NEON) is detected by makefile when the library gets
  compiled. So, if one wants to distribute platform independent binaries, it
  is necessary to compile libefcl.so for different SIMD flavors and
  distribute several different libefcl.so files from which the installer (or
  the main program) would select the right one.

  For CPUs that lack SIMD instructions, there is still a generic C version
  of the code.

  The library can also take the advantage of multi core CPUs to further
  increase its speed by running the computation in multiple threads. It is
  run time configurable how many threads can be used and the library
  adaptively balances the load (even turning itself off on cores overloaded
  by other tasks) so as to gain maximal throughput.

  The library is thread safe, which means that multiple instances of it can
  run at the same time. However, if your program uses fftw library too, care
  must be taken as fftw is not entirely thread-safe. The easiest way to cope
  with it is to use efcl's mutex FFT_mutex and place any non-reentrant fftw
  calls between
        pthread_mutex_lock(&FFT_mutex);
  and
        pthread_mutex_unlock(&FFT_mutex);
  calls.

  The library, although written in C++, can be linked with C programs. It
  does not throw any exceptions.

WHAT IT ISN'T

  To select a channel out of a signal one needs a filter. The efcl
  channelizer expects to be given its impulse response in a file containing
  binary float numbers. The response itself may or may not be symmetric ---
  it does not matter as the filtering is fully general. If you need to use
  minimum phase filter for some reason, it is possible. It is enough to
  specify this filter for channel 0, i.e. the low pass filter --- filters
  for other channels are derived automatically from this one by efcl.

  Although there is a utility simple_filter which produces example filter
  (truncated sigma factor weighted sin(x)/x) it was meant only for debugging
  and performance testing, not for meaningful signal processing.

  Designing a proper filter is much more involved, the crucial thing to
  consider is that the stop band of such a filter must be falling with 1/f
  or better with 1/f^2 so that the stop band would sum to a small constant
  when folded due to aliasing (which happens due to decimation). Otherwise
  the noise and spectral leakage would be much higher than expected.

  Designing such a filter is however beyond the scope of this library. Use
  gnuradio or write your own design tool (weighted Remez algorithm might be
  a method of choice). Keep in mind that the filter length is zero-padded
  towards the nearest higher multiple of C (the number of channels). This
  new length is displayed as L in efcl's verbose mode. Note that those
  zeroes are processed as if they were general numbers, thereby taking a
  processing time. It is therefore advised to use only lengths divisible by
  C when designing the filter so as to use the additional taps.

DEPENDENCIES, ASSUMPTIONS AND LIMITATIONS

  (1) I assumed little endian machine as mixed and big endians are long dead
  anyway (it might still work on big endian machine I only did not care
  about them when writing the program).

  (2) I assumed that storing binary floats to file as they lay in memory is
  OK (which it certainly is as long as the same CPU reads it back, most
  likely even if different CPU does).

  (3) The makefile heavily uses Linux specific /proc/cpuinfo kernel
  interface to learn system configuration for which it is then compiled.
  This might complicate porting it to other UNIXes.

  (4) On modern CPU with constant TSC counter one also needs to enable
  cpufreq statistics so that the kernel interface

     /sys/devices/system/cpu/cpuNR/cpufreq/stats/time_in_state

  would exist. It can be done by adding

        CONFIG_CPU_FREQ_STAT=y
        CONFIG_CPU_FREQ_STAT_DETAILS=y

  to your kernel .config and recompiling the kernel. Note that the
  channelizer would work even without it as this is only needed to compute
  its performance statistics.

  (5) The runtime compiled SSE/AVX/NEON SIMD code assumes *.so ABI format.
  This means that efcl will not run under Cygwin which uses Windows ABI for
  shared libraries.

  (6) To compile the efcl library one needs the following software packages.

     PACKAGE VERSIONS KNOWN TO WORK WITH (*)

     gcc/g++ 3.3.6
     C library (getconf) 2.2.5
     pthread library 0.9
     FFTW library 3.3.3
     nasm 2.11.06
     ld 2.14

     (*) There might be other versions that work too, the listed ones were
     actually tested. Note that nasm and ld are also required at the runtime if
     the library has been configured to use SIMD code.

  (7) It is assumed that memalign() function is available on the system and
  that it allocates aligned memory that can be freed using standard free()
  function (this is OK on Linux but AFAIK, memalign()ed memory, once
  allocated, cannot be freed on Free BSD).

  (8) The multicore load balancing code assumes that the individual CPU
  core's TSC counters are perfectly synchronized and run in constant TSC
  mode (i.e. measuring time). Moreover, it also uses only lower 32 bits for
  computing average speed, which means that the blocks (see the BL constant)
  must be sufficiently small so that their processing takes less than 2^31 TSC ticks.
  This amounts to about 0.5 s on a 4 GHz CPU, which must be enough for
  everyone (usually, this processing takes from 0.01 ms to 10 ms, depending
  on BL, number of channels and filter length).

HOW TO COMPILE AND INSTALL IT

  To get help on what the makefile provides, type

    make

  To install the library, just type

    make install

  and it will compile and install:

       efcl binary to $DESTDIR/usr/local/bin
       libefcl.a and libefcl.so to $DESTDIR/usr/local/lib
       efcl.h header file to $DESTDIR/usr/local/include

  If you wanted a different configuration than the one which was discovered
  by the SIMD_probe script, type

    make clean
    SIMD=<implementation_name> make install

  where the <implementation_name> is one of SSEx86, SSE, AVX, NEON, C1, C2,
  C3, A1, A2, A4. See SIMD variable in pgmdoc.txt for explanation.

USAGE

  The easiest way to use the library is via the efcl program which reads
  input stream, channelizes it and sends the channels to its output. See
  efcl --help to learn how to use it.

  The performance in megasamples per second (MS/s) is the best when the
  number of channels is the power of two. Numbers that can be factorized
  into 2, 3, 5 and 7 work well too. This has something to do with a FFT
  involved in the process.

  For more complicated uses, like several channelizers running at the same
  time, one probably wants to use channelizer() function directly. See
  efcl.h to learn about its interface and alibtest.cc to see how it can be
  statically linked to a C program (linking with C++ is even easier).

HOW TO UNDERSTAND EFCL'S VERBOSE OUTPUT

Unless efcl is run with -q option, it produces long performance report about
its run (used mainly during its development for profiling). For instance,
running

      ./efcl -C=72 -D=50 -F=FIR -t=1 -B=9710 --bench

on a 1.5 GHz Athlon XP might produce something like this:

CHANNELIZER SETUP:
  SSEx86 code compiled (1313+91 bytes), overhang = 2*(6*6+1*0)-72 = 0 csamples
  efcl 0.1 (SSEx86 implementation) compiled by gcc-3.3.6 using fftw-3.3.3
  filter length l=1151, 0-padded to L=1152
  number of channels C=72, downsampling D=50, maximum threads=1
  FFT: add= 912 mul= 216 mac= 216, 21.6667 FLOP/csample
  Polyphase filter: add= 2160 mul= 2304, 62 FLOP/csample
SPEED:
  Throughput in complex valued output samples: 16.28 MS/s
        Complex samples (csamples) generated: 144000000
PERFORMANCE:
     --- per-thread CPU clocks --- MIN AVG MAX AVG per SIMDop
  polyphase filter clocks per csample: 43.14 43.14 43.14 | 5.567 mac
  FFT CPU clocks per 1 output csample: 37.77 37.77 37.77 | 3.487 +|*
  memcpy clocks per 1 output csample: 4.63 4.63 4.63 | 4.626 ld|st
  management clocks per csample: 7.78 7.78 7.78 +-------------
  stall clocks per 1 output csample: 0.71 0.71 0.71
  per thread FFT performance: 0.878218 GFLOPS 0.573618 FLOP/clock
  per thread filter performance: 2.2002 GFLOPS 1.43709 FLOP/clock
  Total performance (all threads): 1.36224 GFLOPS 0.88976 FLOP/clock

The first line informs about the size of the filter and data copying
codelets, respectively. Then there is the filter codelet's overhang which is
SIMD_WIDTH*(W1*R1+W2*R2)-C and informs the user which W1, W2 parameters were
finally used. See pgmdoc.txt for the meaning of those constants.

The second line clarifies the version numbers.

The third line show the filter length l (in samples) and its zero padded
version L, which will be used during runtime.

The 4th line recaps the number of channels, decimation and maximum allowed
number of threads.

The next two lines then show how many floating point operations (additions
or multiplications) is needed to compute a single complex valued sample of
the filter and FFT, on average. Note that FFT numbers come from fftw and it
seems to me that in more modern CPUs these seem to be suspiciously low so
maybe the fftwf_flops() function does not return the number of basic
arithmetic operations but perhaps the number vector operations (contrary to
what the manual claims). Be therefore cautious about FFT FLOPS/csample and
GFLOPS (later in the table).

The next section shows the average speed of the output stream attained
during the efcl's run. It is expressed in millions of complex samples per
second. The total number of these output samples generated during the run is
on the second line of this section. The reason for selecting output stream
speed instead of input is its relative insensitivity to the exact value of
decimation parameter D. Note that the time is measured using the
gettimeofday() function here, which means that it is a real time, not the
CPU time the OS allocated to efcl's run.

Finally, there is a table of how many CPU clocks the certain computations
took. Note that modern CPUs (unlike the old Athlon XP) measure time with
their rdtsc instruction rather than clocks. I try to recover approximate
clock values from this and kernel supplied table of how long the CPU spent
at which clock frequency. Nevertheless, the it should not be taken as being
very precise.

The three columns entitled with MIN MAX refer to the respective clocks in
two threads selected out of many. The MIN column shows the clocks of the
thread that seemed to work the fastest, whereas the MAX column shows the
clocks of the slowest thread (precisely: the number of clocks the slowest
thread processed its jobs divided by the number of complex samples it
processed). The AVG column are the clocks averaged over all threads
(precisely: summed clocks of all the threads divided by the total number of
complex samples processed).

In the rectangle on the right, entitled by AVG per SIMDop there are the AVG
clocks recalculated to show the number of CPU clocks per vector
load-multiply-accumulate operation that appears during the filter
evaluation. Note that this is treated as single vector operation processing
SIMD_WIDTH complex numbers at once even if it is usually implemented by
several instructions (load, multiply, add) instead of single fma instruction.
The next line show a similar thing for FFT (but note that due it my doubts
about fftwf_flops() it is more or less for completeness). The final line in
the box shows how many cycles it takes to move the SIMD_WIDTH vector in or
out the CPU, during data copying.

Finally there are three lines with GFLOPS performance there. The first two
show FFT and filter performance averaged over all working threads (note that
even if certain thread does only a fraction of work than the others only its
performance during the time it actually runs the efcl will be calculated, so
it will not lead to underestimation the true GFLOPS). The final line are the
combined GFLOPS of FFT and the filter summed over all working threads.